## Slide 1: Pulse Programmer Documentation
12/14/2024

## Slide 2: Pulse Programmer Instruction
pulse | data | op code | delay
8-bit 20-bit 4-bit 32-bit
[63:56] [55:36] [35:32] [31:0]

## Slide 3: Programming Words (v1)
command | addr | pulse pattern | DDS | data | op code | delay
4-bit | 12-bit | 8-bit | 8-bit | 12-bit | 4-bit | 32-bit
[79:76] | [75:64] | [63:56] | [55:48] | [47:36] | [35:32] | [31:0]
Need at least 12-bit data for address in GOTO op-code

## Slide 4: Op Codes
0 = No OP
1 = DELAY
2 = LONG DELAY
3 = GOTO
4 = WAIT

## Slide 5: UART Commands
Currently 10 bytes must be transmitted at a time. Should add timeout
4-bit (16) UART commands are possible
0 = Read from RAM (Not Implemented)
1 = Write to RAM
2 = Start
3 = Stop
4 = ???
Todo
  Add software trigger command
  External Clock?

## Slide 6: Clock
125 MHz clock
8 ns resolution
Minimum delay/pulse = 16 ns (2 clock cycles)
Current Baud Rate: 115200
Maximum Baudrate (6,000,000) needs testing